## Slide 1: Future and Emerging Computing Paradigms in Electronics
24th IEEE International Conference on Electronics, Circuits and Systems (ICECS)
Dec. 7th, 2017
Mustafa Altun, PhD
Electronics & Communication Engineering
Istanbul Technical University
Web: http://www.ecc.itu.edu.tr/

## Slide 2: Outline
Challenges in CMOS
How to beat CMOS
  Emerging Technologies
  Emerging Computing
Proposed: bit stream computing
  Inspired by stochastic computing
  Smaller number of transistors
  Applicable to CMOS
  Applicable to large-area electronics
Concluding remarks

## Slide 3: Challenges in CMOS Performance
*Source: Computing’s Energy Problem in ISSCC, http://cpudb.stanford.edu/
Power ~ Vdd2 × C × f
Energy ~ Vdd2 × C
C ~ Cox × W × L
Cox ~ 1/tox
f ~ 1/delay
delay~ W × L × 1/Vdd
* Vdd is limited by transistor threshold voltage
* tox is limited by leakage current
* W and L is limited by controllability
Vdd vs. L
L vs. year
f vs. year
Power vs. year

## Slide 4: Moore’s Law
1963: CMOS
1965: Moore’s Law
  Transistor count doubles every year.
1975: Moore’s Law updated
  Transistor count doubles every two years.
2015: Gordon Moore: «I see Moore’s law dying here in the next decade or so»
2015: Intel confirming the slowdown in pace of advancement, from two to two and a half years.
  Uncertainty, probabilistic phenomena
  Fabrication challenges
  Power challenges
New technologies and computing paradigms emerge, especially in the last decade
“The number of people predicting the death of Moore's law doubles every two years.”

## Slide 5: Emerging Technologies
DNA computing: A test tube of DNA can contain trillions of strands for parallel computing
Adleman’s motivating experiment for traveling salesman problem,1994
DNA strand displacement
DNA Strand Displacement (DSD) tool by Microsoft
Main goal: to beat CMOS
New technologies requiring new computing paradigms
New technologies using CMOS computing paradigm
New computing paradigms adaptable with CMOS technology

## Slide 6: Emerging Technologies
Quantum computing: Theoretically, quantum computers solve RSA-2048 problem in seconds compared to 10 billion years.
RSA numbers are semi-prime numbers used in criptology. For each RSA number n, there exist prime numbers p and q such that n = p × q.
15 = 3 × 5
77 = 7 × 11
4633 = 41 × 113
A real IBM Q quantum processor with 20 qubits can be used online
Cracking RSA keys – up to 200.000 USD Prize.
Main goal: to beat CMOS
New technologies requiring new computing paradigms
New technologies using CMOS computing paradigm
New computing paradigms adaptable with CMOS technology

## Slide 7: Emerging Technologies
Main goal: to beat CMOS
New technologies requiring new computing paradigms
New technologies using CMOS computing paradigm
New computing paradigms adaptable with CMOS technology
“ A person with a new idea is a crank until the idea succeeds.” - Mark Twain

## Slide 8: Emerging Technologies
Main goal: to beat CMOS
New technologies requiring new computing paradigms
New technologies using CMOS computing paradigm
New computing paradigms adaptable with CMOS technology
Nanowire/nanotube transistor
Computing with nanowire/nanotube transistors
Some advantages over CMOS
Interconnection problems
Lack of integration
Fabrication costs
“We can't solve problems by using the same kind of thinking we used when we created them.” - Albert Einstein

## Slide 9: Emerging Computing
Main goal: to beat CMOS
New technologies requiring new computing paradigms
New technologies using CMOS computing paradigm
New computing paradigms adaptable with CMOS technology
Approximate computing: Area and power reduction at the cost of accuracy for applications not requiring high accuracy (image processing, learning)
Exact 1-bit adder (48 Tran.)
App. 1-bit adder (20 Tran.)
Mean filtering with exact and app. 8-bit ripple-carry adders

## Slide 10: Emerging Computing
Main goal: to beat CMOS
New technologies requiring new computing paradigms
New technologies using CMOS computing paradigm
New computing paradigms adaptable with CMOS technology
“It Is not the Strongest of the Species that Survives but the Most Adaptable” - Charles Darwin
PROPOSED COMPUTING PARADIGM:
Bit Stream Computing (BSC)
inspired by Stochastic Computing (SC)

## Slide 11: Probabilistic Computing
Deterministic
Subsequent state of the system is determined deterministically
Probabilistic
Subsequent state of the system is determined probabilistically
Deterministic
Deterministic
Deterministic
Probabilistic

## Slide 12: Why Probabilistic Computing?
Strengths
  Easier to implement arithmetic operations.
  Circuit size is small and independent of the number of input bits.
  Suitable for applications not requiring high accuracy (image processing, learning).
Weaknesses
  Accuracy problems.
  Long computational times.
  Costly random number generators are needed.

## Slide 13: Why Stochastic Computing?
Easier to implement arithmetic operations.
Stochastic computing (SC) depends on randomly or Binomially distributed bit streams.
0,1,0,1,1,0,1,0
Random Bit Streams
P(x=1) = 4/8
x
0,1,0,0,0,1,0,0
P(y=1) = 2/8
y
Stochastic Computing
x=4/8
y=2/8
z
AND

## Slide 14: Why Stochastic Computing?
Stochastic circuit
Probabilistic
Probabilistic
Deterministic
p1=2/6, p2=2/6, p3=2/6, p4=1/6, p5=5/6, p6=2/6

## Slide 15: Arithmetic Operations with SC
Multiplication: : x x y = z
AND
3-bit deterministic multiplier (30 gates)
3-bit stochastic multiplier (1 gate)
x=(0.100)2
y=(0.100)2
z=(0.010)2
Area cost of an n bit multiplier?
At least how many stream bits for an n bit multiplier?

## Slide 16: Arithmetic Operations with SC
Scaled addition: : z=x(s) + y(1-s), s=0.5
x
y
s
z
MUX
1,1,1,1,1,0,1,1
0,0,1,0,0,1,1,0
1,0,0,1,0,1,0,1
1,0,1,1,0,0,1,1
MUX
x=7/8, y=3/8, s=4/8, z=5/8
1
0
1
0
Averaging the inputs

## Slide 17: Why Stochastic Computing?
Circuit size is small and independent of the number of input bits.
How about considering the cost of random number generators?
Each input needs a separate generator, generally LFSR based.
Conventional Binary
Computing
Stochastic Computing
  Area
  Resolution
  Area
  Resolution

## Slide 18: Input Dependency of SC
x=4/8
x=4/8
z
AND
0,1,0,1,1,0,1,0
z=4/8
0,1,0,1,1,0,1,0
0,1,0,1,1,0,1,0
Input streams are independent
Each input requires a separate generator

## Slide 19: Accuracy of SC
x=4/8
y=2/8
z
AND
0,1,0,0,0,1,0,0
0,1,0,1,1,0,1,0
0,1,0,0,1,0,0,0
0,1,0,1,1,0,1,0
z=1/8
z=2/8
1,0,0,0,0,1,0,0
0,1,0,1,1,0,1,0
z=0/8
Which one is right?

## Slide 20: Accuracy of SC
Explains why SC could not become a real competitor to conventional computing although it offers significant area advantage.
Low accuracy or long computing times is the main obstacle in front of SC.
The longer the streams the more accurate the computing.
1 gate vs. 1000 gates doing the same job having the same accuracy

## Slide 21: Performance of Randomness
Ingredients of “Çiğ Köfte”
Kneading “Çiğ Köfte”
Ready to serve “Çiğ Köfte”
The longer the kneading time the tastier the “Çiğ Köfte”.
The longer the kneading time the more homogeneous (accurate) the “Çiğ Köfte”.
Heterogeneous to Homogeneous: HOW?

## Slide 22: Performance of SC
The longer the bit streams the more accurate the computation.
The longer the bit streams the slower the computation.
0,1,0,1,1,0,1,0,…..
Bit Streams
Perfect accuracy (100%) requires infinite number of bits.

## Slide 23: Bit Stream Computing (BSC)
Exploits the logic used in stochastic computing, but not necessarily employ randomly distributed bit streams.
To improve accuracy and relatively to decrease computing times.
Much smaller arithmetic circuits compared to conventional binary ones
0,1,0,1,1,0,1,0,…..
Bit Streams

## Slide 24: Accurate Adder with BSC
Delay block and an OR gate
Adder with 4 bit inputs and 8 bit output
Delay amount is the time duration of the input stream
n bit input
2n bit output
100% accurate
Area comp. O(n)

## Slide 25: Delay Block
Delay is achieved with inverter chains.
n bit delay needs n inverters

## Slide 26: Accurate Multiplier with BSC
Multiplier with 4 bit inputs and 16 bit output
n bit input
n2 bit output
100% accurate
Area comp. O(n2)

## Slide 27: Semi-Accurate Adder with BSC
n bit input
n bit output
Almost 100% accurate
Area comp. O(1)

## Slide 28: Summary of the Proposed

## Slide 29: Summary of the Proposed
Upto 10X area improvement compared to conventional binary circuits
Proposed adders and multipliers justified in artificial neural networks
This study opens up new horizons for computing with much smaller yet accurate arithmetic circuits.

## Slide 30: Future Works
Perform more detailed CMOS simulations followed by fabrications by considering area, delay, power, and accuracy with timing variations.
Use the proposed circuits in printable, flexible, or organic electronics that requires small number of transistors.

## Slide 31
THANK YOU!
Web: http://www.ecc.itu.edu.tr/
This work is part of a project that has received funding from the European Union's H2020 research and innovation programme under the Marie Skłodowska-Curie grant agreement No 691178.
This work is supported by the TUBITAK-Career project #113E760, and the TUBITAK-1001 project #116E250.