## Slide 1: EHB 111E NANOELECTRONICS
Nanoelectronics, 18/11/2014
FALL 2014
Mustafa Altun
Electronics & Communication Engineering
Istanbul Technical University
Web: http://www.ecc.itu.edu.tr/

## Slide 2: What is Nanoelectronics?
Nano Electronics
1 nm = 10-9m = 10 angstroms.
Atomic Van der Waals radius r: 0.3 to 3 angstroms.
Silicon Van der Waals radius: 2 angstroms.
Diameter of DNA helix: 2nm.,
Thickness of a cell membrane: 7.5nm.
Currently, commercially used, the smallest CMOS technology: 22nm.
Thickness of a human hair: 50um = 50000nm.
Human hair
Sphere model of an atom
DNA helix

## Slide 3: What is Nanoelectronics?
Example:
Consider a human hair with a thickness of 50um. Suppose that the shape of a human hair is cylinder. Consider a nano transistor with dimensions of L=30nm, W=30nm, and H=10nm. How many transistors can we fit into a 1mm human hair?
> 200,000,000,000
Practically, where are we now?
Apple A7 chip in iphone5S has "over 1 billion" transistors that fit in a die area of 100 square millimeters.

## Slide 4: What is Nanoelectronics?
Nano Electronics
Electrical engineering
  HIGH VOLTAGE/CURRENT
  Power transmissions
  Electrical machines
Electronics engineering
  LOW VOLTAGE/CURRENT
  Computers
  Integrated circuits
Electronics
Electrical

## Slide 5: What is Nanoelectronics?
  New future technologies
  Disruptive, completely new (disrupt an existing market)
  In an exploratory phase, not commercially used
  Beyond CMOS devices
Nanowire transistor
Spin wave switch
Single electron transistor
Nanoelectronics is not exactly nanoscale electronics, but emerging and nanoscale electronics.

## Slide 6: Why Nanoelectronics?
CMOS shrinking problems
  Moore’s Law’s anticipated limit, approaching the size of atoms
  Short channel affects and leakage
  Uncertainty, probabilistic phenomena
  Fabrication challenges
  10nm is seen as critical point
Non-stinky socks
Water resistant cloths
Main goal: to beat CMOS

## Slide 7: Why Nanoelectronics?
Top-Down
  From a stone to a sculpture
  More accurate
  Lithography based
  Traditional
  Hard-to-manipulate in nanoscale
Top-Down vs. Bottom-Up Fabrication
Bottom-Up
  From separate molecular materials to an organized structure
  Self-assembly
  Regular arrays
  More efficient
Self-assembled circuit with 64,000 elements in three minutes

## Slide 8: Why Nanoelectronics?
Probabilistic phenomena
  Every physical behavior is probabilistic!
  The smaller the more probabilistic
Example:
  A transistor with 1 electron vs. 10 electrons vs. 100,000 electrons in conduction. When applied a controlling gate voltage of 1V, each electron passes from source to drain with a probability of 0.9. What are the probabilities that the transistor conduct current (at least one electron passes from source to drain)?

## Slide 9: Nanoelectronics Research
Dramatic increase in interest and funding of nanoelectronics.
Top funding agencies (Horizon 2020-$20b, NSF-$7b, NIH- $30b, Tubitak- $1b …) pour money to nanoengineering and nanoscience.
  Leading universities have research groups on nanoelectronics.
  The most prestigious conferences on circuit design DAC and ICCAD have increasing number of papers targeting nanotechnologies.
Better to add the word “nano” to your paper/presentation/proposal!

## Slide 10: Computational Nanoelectronics
Theoretical
  Physics rules – probability based
  Quantum mechanics
    The uncertainty principle
  Schrödinger equation
  Theory of relativity
Experimental
  Fabrication processes
  Self assembly
Computational
  Computing 0s 1s
  Achieve logic operations AND OR

## Slide 11: Computational Nanoelectronics
Nanocomputers get real
Ultra-tiny computer from an assembly of nanowires, Harvard University

## Slide 12: Emerging Electronic Devices

## Slide 13: Quantum Computing
Theoretically, quantum computers solve RSA-2048 problem in seconds compared to 10 billion years.
Shor’s algorithm.
Cracking RSA keys.
Would be a breakthrough in cryptology.
Practically, where are we now?
Erik Lucero’s circuit to factorize 15

## Slide 14: Bits vs. Qubits
Bits
0 or 1 at a time
Deterministic
Discrete and stable states
State of a bit:
In state 0 or 1 with a probability of
Qubits
0 or 1 at the same time
Probabilistic
Superposition of states
State of a qubit:
In state 0 with a probability of
In state 1 with a probability of

## Slide 15: Quantum Computing
February 2012: IBM scientists achieved several breakthroughs in quantum computing with superconducting integrated circuits
September 2012: The first working "quantum bit" based on a single atom in silicon suitable for the building blocks of modern computers.
October 2012: Nobel Prizes were presented to David J. Wineland and Serge Haroche for their basic work on understanding the quantum world - work which may eventually help makequantum computing possible.
May 2013: Google launching the Quantum Artificial Intelligence Lab with 512-qubit quantum computer.

## Slide 16: DNA Computing
Parallel computing
  For certain problems, DNA computers are faster and smaller than any other computer built so far.
  A test tube of DNA can contain trillions of strands.
Computing with DNA strands
  Depending on absence and presence of DNA molecules.
  Strands have directions.
  How do strands stick together?

## Slide 17: DNA Computing
Main advantages
  Parallel
  Dense, small area
  Can solve untractable problems
Disadvantages
  Slow
  Fragile
  Unreliable, randomness

## Slide 18: Computing with Nano Arrays
Self-assembled nano arrays
Computing models for nano arrays
  Two-terminal switch-based
    Diode-based
    Transistor-based
  Four-terminal switch-based

## Slide 19: Computing with Seperate Devices
Nanowire transistor
Single electron transistor
Direct replacement of CMOS transistors
Some advantages over CMOS
Interconnection problems
Lack of integration

## Slide 20: Suggested Readings/Videos
Feynman, R. P. (1960). There's plenty of room at the bottom. Engineering and Science, 23(5), 22-36.
Richard Feynman Nanotechnology Lecture, 1984
http://www.youtube.com/watch?v=4eRCygdW--c

## Slide 21: Our Group Information
State-of-the-art research
  Nanoarrays
  DNA computing
  Quantum computing
  Stochastic computing
Make you think out of the box
Unconventional
Math and circuit based, especially the probability theory
Emerging Circuits and Computation
http://www.ecc.itu.edu.tr/