## Slide 1: ELE 523E COMPUTATIONAL NANOELECTRONICS
W6: Probabilistic Computing, 24/10/2016
FALL 2016
Mustafa Altun
Electronics & Communication Engineering
Istanbul Technical University
Web: http://www.ecc.itu.edu.tr/

## Slide 2: Outline
Overview of probabilistic computing
  Strengths
  Weaknesses
  Application areas
Stochastic computing with logic gates
  Circuit analysis
  Synthesis of stochastic inputs
  Synthesis of polynomial functions
Probabilistic switches
  Two-terminal switches
  Four-terminal switches and percolation

## Slide 3: Probabilistic Computing
Deterministic
Subsequent state of the system is determined deterministically
Probabilistic
Subsequent state of the system is determined probabilistically
Deterministic
Deterministic
Deterministic
Probabilistic

## Slide 4: Why Probabilistic Computing?
Strengths
  Easier to implement arithmetic operations.
  Works efficiently in encoding/decoding
  High degree of transient error tolerance.
  Exploit randomness that is a fact in nanoscale.
  Used in modeling probabilistic behavior of nanotechnologies.
Weaknesses
  Accuracy problems.
  Long computational times.

## Slide 5: Stochastic Computing
Stochastic computing (SC) is a probability computing that depends on random bit streams.
0,1,0,1,1,0,1,0
Random Bit Streams
P(x=1) = 4/8
x
0,1,0,0,0,1,0,0
P(y=1) = 2/8
y
Stochastic Computing
x=4/8
y=2/8
z
AND

## Slide 6: Random Bit Streams
Randomly assigning each bit value
CONVENTIONAL
The stream probability p represents the probability of having 1 for each bit
The stream has a binomial distribution in terms of the number of 1s
Less accurate
Perfectly random
Randomly shuffling a bit stream
The stream probability p represents (total number of 1s)/(total number of bits)
The stream has a deterministic behaviour in terms of number of 1s
More accurate
The longer the streams the closer these methods.

## Slide 7: Stochastic Computing
Stochastic circuit
Probabilistic
Probabilistic
Deterministic
p1=2/6, p2=2/6, p3=2/6, p4=1/6, p5=5/6, p6=2/6

## Slide 8: Accuracy of SC
x=4/8
y=2/8
z
AND
0,1,0,0,0,1,0,0
0,1,0,1,1,0,1,0
0,1,0,0,1,0,0,0
0,1,0,1,1,0,1,0
z=1/8
z=2/8
1,0,0,0,0,1,0,0
0,1,0,1,1,0,1,0
z=0/8
Which one is right?

## Slide 9: Accuracy of SC
x=4/8
x=4/8
z
AND
0,1,0,1,1,0,1,0
z=4/8
Dependency is important!
0,1,0,1,1,0,1,0
0,1,0,1,1,0,1,0
Conventionally, input streams are independent

## Slide 10: Accuracy of SC
Randomly assigning each bit value
CONVENTIONAL
The stream probability p represents the probability of having 1 for each bit
The stream has a binomial distribution
Randomly shuffling a bit stream
The stream probability p represents (total number of 1s)/(total number of bits)
Calculate the error as
Calculate the error rate?
AND

## Slide 11: Randomly Assigning
x=2/4
y=2/4
AND
Example:
Consider 4-bit input bit streams x and y such that each bit is 1 with an independent probability of p=1/2.
Find the probability of accurate computation z=1/4.
Find the probability of having z=0/4.
Find the probability of having z=2/4.
Find the probability of having z=3/4.
Find the probability of having z=4/4.
Find the everage error rate.
z

## Slide 12: Randomly Shuffling
x=2/4
y=2/4
AND
Example:
Consider randomly distributed 4-bit input bit streams x and y such that half of its bits are 1 and the other half 0.
Find the probability of accurate computation z=1/4.
Find the probability of having z=0/4.
Find the probability of having z=2/4.
Find the probability of having z=3/4.
Find the probability of having z=4/4.
Find the everage error rate.
z

## Slide 13: Improving the Accuracy
Using correlated bit streams
Using quasi-random bit streams
Low-discrepancy vs. random sequence
Error-free computing
1 gate vs. 1000 gates doing the same job

## Slide 14: Defect Tolerance in SC
x=4/8=(0.100)2
y=2/8=(0.010)2
AND
What if there is a bit-flip in an input?
z=1/8=(0.001)2
0,1,0,0,0,1,0,0
0,1,0,1,1,0,1,0
z=1/8
(0.100)2 x (0.010)2 = (0.001)2

## Slide 15: Performance of Randomness
Ingredients of “Çiğ Köfte”
Kneading “Çiğ Köfte”
Ready to serve “Çiğ Köfte”
The longer the kneading time the tastier the “Çiğ Köfte”.
The longer the kneading time the more homogeneous (accurate) the “Çiğ Köfte”.
Heterogeneous to Homogeneous: HOW?

## Slide 16: Performance of SC
The longer the bit streams the more accurate the computation.
The longer the bit streams the more reliable the computation.
The longer the bit streams the slower the computation.
0,1,0,1,1,0,1,0,…..
Bit Streams

## Slide 17: Arithmetic Operations with SC
Multiplication: : x x y = z
AND
3-bit deterministic multiplier (30 gates)
3-bit stochastic multiplier (1 gate)
x=(0.100)2
y=(0.100)2
z=(0.010)2
At least how many bits shoud a stream have?
At least how many stream bits for an n-bit multiplier?

## Slide 18: Arithmetic Operations with SC
Scaled addition: : x(s) + y(1-s) = z
x
y
s
z
MUX
1,1,1,1,1,0,1,1
0,0,1,0,0,1,1,0
1,0,0,1,0,1,0,1
1,0,1,1,0,0,1,1
MUX
x=7/8, y=3/8, s=4/8, z=5/8
1
0
1
0

## Slide 19: Arithmetic Operations with SC
Example:
Find the expression of z for both stochastic and deterministic inputs applied.
x1
x2
x3
x4
z
1
0
AND
MUX
NOT

## Slide 20: Synthesis Problem-1
Problem: How to construct a logic circuit in order to implement given output probabilities with a set of input probabilities?
P(x = 1) = 0.4
P(z = 1) = 0.6
1,0,1,1,0,1,0,0,0,0
0,1,0,0,1,0,1,1,1,1
P(z = 1) = P(x = 0)
P(x = 1) = 0.4
P(z = 1) = 0.2
0,1,0,1,0,0,1,1,0,0
0,0,0,1,0,0,1,0,0,0
P(z = 1) = P(x = 1) P(y = 1)
1,0,1,1,0,0,1,0,0,1
P(y = 1) = 0.5
P(x = 1) = 0.4
P(z = 1) = 0.3
0,0,1,0,1,0,1,0,1,0
0,1,0,0,0,1,0,0,0,1
P(z = 1) = P(x = 0) P(y = 0)
1,0,0,1,1,0,0,1,1,0
P(y = 1) = 0.5
Example:
Implement output probabilities 0.6, 0.2, and 0.3 with using input probabilities of 0.4 and 0.5.

## Slide 21: Synthesis Problem-1
Theorem (Qian et al. 2011): With input probabilities = {0.4, 0.5}, we can synthesize arbitrary decimal output probabilities.
Example: Synthesize q = 0.757
(Black dots are inverters)

## Slide 22: Synthesis Problem-2
Problem: How to construct a logic circuit in order to implement a polynomial g(t) where both t and g(t) are in unit interval?

## Slide 23: Synthesis Problem-2
Example:
Implement g(t) = 3/8 t2 + 5/8 t.
AND
MUX
1
0
t
t
3/8
t
g(t)

## Slide 24: Synthesis Problem-2
Example:
Implement g(t) = t3 – 2t2 + 1.
NOR
MUX
1
0
t
t
t
1
g(t)

## Slide 25: Synthesis Problem-2
Example:
Implement g(t) = 9/4 t2 – 15/8 t + 5/8 and test on g(1/2).
t
t
5/8
g(t)
t
MUX
0
1
2
3
0
1/8
1

## Slide 26: Synthesis Problem-2
Theorem (Qian et al. 2012): With using Bernstein polynomials, we can synthesize any polynomial g(t).
g(t) = 9/4 t2 – 15/8 t + 5/8
= 5/8 B0 + 0 B1 + 1/8 B2 + 1 B3
Bi = probability that the output of the adding unit is i.
B0 = (1-t)3
B1 = 3 t(1-t)2
B2 = 3 t2(1-t)
B3 = t3
Example:
Implement g(t) = 9/4 t2 – 15/8 t + 5/8.

## Slide 27: Probabilistic Two-Terminal Switch
0,1,0,1,1,0,1,0
P(x=1) = p = 4/8
x
A probabilistic switch is ON with a probability of p.
Can be implemented with stochastic bit streams.
Can be used to model probabilistic phenomena in nanoscale such as random defects.

## Slide 28: Probabilistic Two-Terminal Switch
A probabilistic MOS is a probabilistic switch.
* Probabilistic CMOS technology: A survey and future directions

## Slide 29: Probabilistic Two-Terminal Switch

## Slide 30: Synthesis Problem
Problem: How to construct a circuit in order to implement a given binary decimal numbers using p-switches with p=1/2 ?
Example:
Implement the output probabilities 0.112 and 0.0112 with p-switches with p=1/2.
0.0112
0.112

## Slide 31: Synthesis Problem
Progressing from the least-significant to the most-significant bits
Example:
Implement the output probability 0.10112 with p-switches with p=1/2.

## Slide 32: Synthesis Problem
Binary tree showing how to generate all possible switching circuits
(Wilhelm et al. 2008)

## Slide 33: Probabilistic Four-Terminal Switch
0,1,0,1,1,0,1,0
P(x=1) = p = 4/8
x
A probabilistic switch is ON with a probability of p.
Can be implemented with stochastic bit streams.
Can be used to model probabilistic phenomena in nano-crossbar arrays such as random defects.

## Slide 34: Probabilistic Four-Terminal Switch
Find the probability of having a path between top-bottom and left-right plates.
How to find the probabilities for larger sizes?
For larger sizes is the probabilistic phenomena increase or decrese?
Use «Percolation Theory»

## Slide 35: Percolation Theory
pT-B versus p for 1×1, 2×2, 6×6, 24×24, 120×120, and infinite size lattices.
Each square, representing a four-terminal switch, in the lattice/array is colored black with independent probability p.
pT-B is the probability that a connected path exists between the top and bottom plates.

## Slide 36: Percolation Theory
Rich mathematical topic that forms the basis of explanations of physical phenomena such as diffusion and phase changes in materials.
Broadbent & Hammersley (1957).

## Slide 37: Percolation Theory
Sharp non-linearity in global connectivity as a function of random local connectivity.

## Slide 38: Margins
One-margin: Tolerable p1 ranges for which we interpret p2 as logical one.
Zero-margin: Tolerable p1 ranges for which we interpret p2 as logical zero.
Margins correlate with the degree of deterministic phenomena.

## Slide 39: Suggested Readings
Qian, W., & Riedel, M. D. (2008, June). The synthesis of robust polynomial arithmetic with stochastic logic. In Design Automation Conference, 2008. DAC 2008. 45th ACM/IEEE (pp. 648-653). IEEE.
Alaghi, A., & Hayes, J. P. (2013). Survey of stochastic computing. ACM Transactions on Embedded Computing Systems (TECS), 12(2s), 92.
Vahapoglu, E., & Altun, M. (2016, July). Accurate Synthesis of Arithmetic Operations with Stochastic Logic. In VLSI (ISVLSI), 2016 IEEE Computer Society Annual Symposium on (pp. 415-420). IEEE.
Wilhelm, D., & Bruck, J. (2008, July). Stochastic switching circuit synthesis. In Information Theory, 2008. ISIT 2008. IEEE International Symposium on(pp. 1388-1392). IEEE.
Article on probabilistic CMOS: http://www2.technologyreview.com/news/409597/tr10-probabilistic-chips/
Moore, E. F., & Shannon, C. E. (1956). Reliable circuits using less reliable relays. Journal of the Franklin Institute, 262(3), 191-208.