## Slide 1: ELE 523E COMPUTATIONAL NANOELECTRONICS
W4: Computing with Nano Arrays, 17/10/2016
FALL 2016
Mustafa Altun
Electronics & Communication Engineering
Istanbul Technical University
Web: http://www.ecc.itu.edu.tr/

## Slide 2: Outline
Computing with nano arrays
  Self-assembly
  Two-terminal vs. four-terminal
Arrays of two-terminal devices
  Diode based
  Transistor based
Arrays of four-terminal devices

## Slide 3: Self-assembly
From disordered to ordered and regular structure

## Slide 4: Why Self-assembly?
We prefer order to disorder.
Living cells self-assemble.
Self-assembly is practical to manufacture nano structures.
Self-assembled nano structures

## Slide 5: Why Self-assembly?
Directed assembly
  Advantages
    Results in a functional construct from a print/layout
  Disadvantages
    Costly in nanoscale
    Time consuming
Self assembly
  Advantages
    Fast and efficient in nanoscale
    Results in condensed structures
  Disadvantages
    Not results in a functional construct

## Slide 6: Research on Self-assembly
Video-1: Self-Assembly of Lithographically Patterned 3D Micro/Nanostructures
Lab: Gracias Lab
University: John Hopkins University
URL: http://www.youtube.com/watch?v=GL0im9b6GgU
Video-2: It's Not Magic: Watch How Smart Parts Self-Assemble
Lab: Self-assembly Lab
University: Massachusetts Institute of Technology (MIT)
URL: http://www.youtube.com/watch?v=GIEhi_sAkU8
VİDEOS FROM LABS:

## Slide 7: Nano Arrays
SELF
ASSEMBLY
REGULAR
NANO
ARRAYS

## Slide 8: Modelling Nano Arrays

## Slide 9: Two-terminal Diode-based Model

## Slide 10: Two-terminal Diode-based Model
Example:
Implement the Boolean function f = A+B with diode based nanoarrays.
Diode-resistor logic

## Slide 11: Two-terminal Diode-based Model
Example:
Implement the Boolean function f = A B with diode based nanoarrays.
Diode-resistor logic

## Slide 12: Two-terminal Diode-based Model
Example:
Implement the Boolean function f = A B + C D with diode based nanoarrays.

## Slide 13: Two-terminal FET-based Model
From Snider, G., et al., (2004). CMOS-like logic in defective, nanoscale crossbars. Nanotechnology.

## Slide 14: Two-terminal FET-based Model
Example:
Implement the Boolean function f = Aꞌ with CMOS based nanoarrays.

## Slide 15: Two-terminal FET-based Model
Example:
Implement the Boolean function f = (A B + C D)ꞌ with CMOS based nanoarrays.

## Slide 16: Two-terminal vs. Four-terminal
Shannon’s work: A Symbolic Analysis of Relay and Switching Circuits(1938)

## Slide 17: Two-terminal vs. Four-terminal

## Slide 18: Two-terminal vs. Four-terminal
What are the Boolean functions implemented in (a) ad (b)?

## Slide 19: A Lattice of Four-terminal Switches
3 × 3 2D switching network and its lattice form

## Slide 20: Four-terminal Switch-based Model
Switches are controlled by Boolean literals.
fL evaluates to 1 iff there exists a top-to-bottom path.
gL evaluates to 1 iff there exists a left-to-right path.

## Slide 21: Logic Synthesis Problem
How can we implement a given target Boolean function fT with a lattice of four-terminal switches?
Example: fT = x1x2x3+x1x4

## Slide 22: Logic Synthesis Problem
Example: fT = x1x2x3+x1x4+x1x5
9 TOP-TO-BOTTOM PATHS!

## Slide 23: Synthesis Method
Example: fT = x1x2x3+x1x4+x1x5
fTD = (x1+x2+x3)(x1+x4)(x1+x5)
fTD = x1 + x2x4x5 + x3x4x5
Start with fT and its dual.
Assign each product of fT to a column.
Assign each product of fT D to a row.
Compute an intersection set for each site.
Arbitrarily select a literal from an intersection set and assign it to the corresponding site.

## Slide 24: Synthesis Method

## Slide 25: Math Behind the Method – Theorem 1
Theorem 1 (Altun and Riedel, 2010): If fT and fTD are implemented as subsets of all top-to-bottom and left-to-right paths, respectively, then fL = fT and gL = fTD.

## Slide 26: Math Behind the Method – Theorem 1
Theorem 1 allows us to only consider column-paths. We do not need to enumerate all paths!

## Slide 27: Math Behind the Method – Theorem 2
Theorem 2 (Altun and Riedel, 2010): Consider a product Pi of fT in ISOP form. For any literal x of Pi there exists at least one product Pj of fTD such that Pi ∩ Pj = x.
Lemma (Fredman and Khachiyan, 1996): Consider products Pi and Pj of fT and fTD in ISOP forms, respectively. Pi ∩ Pj ≠ Ø

## Slide 28: Math Behind the Method – Theorem 2
Theorem 2 (Altun and Riedel, 2010): Consider a product Pi of fT in ISOP form. For any literal x of Pi there exists at least one product Pj of fTD such that Pi ∩ Pj = x.
Each column is for each product!

## Slide 29: Method’s Performance
Size of the lattice: m×n
The time complexity:
O(m2n2)
n and m are the number of products of the target function fT and its dual fTD, respectively.

## Slide 30: Implementing Parity Functions
A Parity function f evaluates to 1 iff the number of variables assigned to 1 is an odd number:

## Slide 31: Implementing Parity Functions

## Slide 32: Implementing Parity Functions
Lattice size: (log m +1)×n
compared to m×n
n and m are the number of products of the target function fT and its dual fTD, respectively.

## Slide 33: Implementing parity functions
OPTIMAL
Lattice size: (log m +1)×n= (log 4 +1)×4=12
Lattice size: 3×3=9
XOR3
XOR3

## Slide 34: Implementing parity functions
OPTIMAL
Lattice size: (log m +1)×n= (log 8 +1)×8=32
Lattice size: 3×5=15

## Slide 35: Optimal Lattice Sizes
We need at least 3 rows to implement the target functions.
Can we implement the target functions with 2 columns?
NO for fT1; YES for fT2.
The minimum lattice sizes for fT1 and fT2 are 9 and 6.

## Slide 36: Suggested Readings
Shannon, C. E. (1938). A symbolic analysis of relay and switching circuits. Electrical Engineering, 57(12), 713-723
Whitesides, G. M., & Grzybowski, B. (2002). Self-assembly at all scales.Science, 295(5564), 2418-2421.
Snider, G., Kuekes, P., Hogg, T., & Williams, R. S. (2005). Nanoelectronic architectures. Applied Physics A, 80(6), 1183-1195.
Altun, M., & Riedel, M. D. (2012). Logic synthesis for switching lattices.Computers, IEEE Transactions on, 61(11), 1588-1600.
Strukov, D. B., & Likharev, K. K. (2012). Reconfigurable nano-crossbar architectures. Nanoelectronics and Information Technology, 543-562.