## Slide 1: ELE 523E COMPUTATIONAL NANOELECTRONICS
W1: Introduction, 19/9/2016
FALL 2016
Mustafa Altun
Electronics & Communication Engineering
Istanbul Technical University
Web: http://www.ecc.itu.edu.tr/

## Slide 2: What is Nanoelectronics?
Nano Electronics
1 nm = 10-9m = 10 angstroms.
Atomic Van der Waals radius r: 0.3 to 3 angstroms.
Silicon Van der Waals radius: 2 angstroms.
Diameter of DNA helix: 2nm.,
Thickness of a cell membrane: 7.5nm.
Currently, commercially used, the smallest CMOS technology: 14nm.
Thickness of a human hair: 50um = 50000nm.
Human hair
Sphere model of an atom
DNA helix

## Slide 3: What is Nanoelectronics?
Example:
Consider a human hair with a thickness of 50um. Suppose that the shape of a human hair is cylinder. Consider a nano transistor with dimensions of L=30nm, W=30nm, and H=10nm. How many transistors can we fit into a 1mm human hair?
> 200,000,000,000
Practically, where are we now in 2016?
A10 Fusion chip in Iphone7 has "over 3.3 billion" transistors with TSMC FinFET 16nm technology that fit in a die area of 150 square millimeters.

## Slide 4: What is Nanoelectronics?
Nano Electronics
Electrical engineering
  HIGH VOLTAGE/CURRENT
  Power transmissions
  Electrical machines
Electronics engineering
  LOW VOLTAGE/CURRENT
  Computers
  Integrated circuits
Electronics
Electrical

## Slide 5: What is Nanoelectronics?
  New future technologies
  Disruptive, completely new (disrupt an existing market)
  In an exploratory phase, not commercially used
  Beyond CMOS devices
Nanowire transistor
Spin wave switch
Single electron transistor
Nanoelectronics is not exactly nanoscale electronics, but emerging and nanoscale electronics.
FinFET transistor

## Slide 6: Why Nanoelectronics?
CMOS shrinking problems
  Moore’s Law’s anticipated limit, approaching the size of atoms
  Short channel affects and leakage
  Uncertainty, probabilistic phenomena
  Fabrication challenges
  Power challenges
  10nm is seen as a critical point
Non-stinky socks
Water resistant cloths
Main goal: to beat CMOS technology

## Slide 7: Moore’s Law
1963: CMOS
1965: Moore’s Law
  Transistor count doubles every year.
1975: Moore’s Law updated
  Transistor count doubles every two years.
2015: Gordon Moore: «I see Moore’s law dying here in the next decade or so»
2015: Intel confirming the slowdown in pace of advancement, from two to two and a half years.
  Uncertainty, probabilistic phenomena
  Fabrication challenges
  Power challenges
New technologies emerge

## Slide 8: Critical Limits in Circuit Performance
*Source: Computing’s Energy Problem in ISSCC, http://cpudb.stanford.edu/
Power ~ Vdd2 × C × f
Energy ~ Vdd2 × C
C ~ Cox × W × L
Cox ~ 1/tox
f ~ 1/delay
delay~ W × L × 1/tox
* Vdd is limited by transistor threshold voltage
* tox is limited by leakage current
* W and L is limited by controllability
Vdd vs. L
L vs. year
f vs. year
P vs. year

## Slide 9: Why Nanoelectronics?
Top-Down
  From a stone to a sculpture
  More accurate
  Lithography based
  Traditional
  Hard-to-manipulate in nanoscale
Top-Down vs. Bottom-Up Fabrication
Bottom-Up
  From separate molecular materials to an organized structure
  Self-assembly
  Regular arrays
  More efficient
Self-assembled circuit with 64,000 elements in three minutes

## Slide 10: Why Nanoelectronics?
Probabilistic phenomena
  Every physical behavior is probabilistic!
  The smaller the more probabilistic
Example:
  A transistor with 1 electron vs. 10 electrons vs. 100,000 electrons in conduction. When applied a controlling gate voltage of 1V, each electron passes from source to drain with a probability of 0.9. What are the probabilities that the transistor conduct current (at least one electron passes from source to drain)?

## Slide 11: Nanoelectronics Research
Dramatic increase in interest and funding of nanoelectronics.
Top funding agencies (Horizon 2020-$20b, NSF-$7b, NIH- $30b, Tubitak- $1b …) pour money to nanoengineering and emerging computing.
  Leading universities have research groups on nanoelectronics.
  The most prestigious conferences on circuit design DAC, ICCAD, DATE, and ISSCC have increasing number of papers targeting emerging technologies.
Better to add the word “nano and emerging” to your paper/presentation/proposal!

## Slide 12: Computational Nanoelectronics
Theoretical
  Physics rules – probability based
  Quantum mechanics
    The uncertainty principle
  Schrödinger equation
  Theory of relativity
Experimental
  Fabrication processes
  Self assembly
Computational
  Computing 0s and 1s
  Achieve logic and memory operations

## Slide 13: Computational Nanoelectronics
Nanocomputers get real
Ultra-tiny computer from an assembly of nanowires, Harvard University

## Slide 14: Suggested Readings/Videos
Feynman, R. P. (1960). There's plenty of room at the bottom. Engineering and Science, 23(5), 22-36.
Iwai, H. I. R. O. S. H. I. (2009). Roadmap for 22nm and beyond.Microelectronic Engineering, 86(7), 1520-1528.
Conte, T.; Gargini, P. (2015), On The Foundation Of The New Computing Industry Beyond 2020, IEEE, International Technology Roadmap for Semiconductors (ITRS)
Richard Feynman Nanotechnology Lecture, 1984
http://www.youtube.com/watch?v=4eRCygdW--c

## Slide 15: Course Information
A research course
Make you think out of the box
Unconventional
Math and circuit based icluding the probability theory
http://www.ecc.itu.edu.tr/index.php/ELE_523E