## Slide 1: ELE 523E COMPUTATIONAL NANOELECTRONICS
W10-W11: Fault Tolerance, 21/11/2016-28/11/2016
FALL 2016
Mustafa Altun
Electronics & Communication Engineering
Istanbul Technical University
Web: http://www.ecc.itu.edu.tr/

## Slide 2: Outline
Faults in Nano-crossbar arrays
  Diode-based
  FET-based
  Four-terminal switch based
Fault Tolerance Stages
  Fabrication
  Post-fabrication
  In-field
Post-fabrication and Defects in Nano-crossbar arrays
  Reconfiguration of a circuit
  Mapping with defects
    Defect-aware
    Defect-unaware
Analysis of in-field Transient Faults in Nano-crossbar arrays
  Diode-based
  FET-based
  Four-terminal switch based
General Transient Fault Tolerance Techniques
  Multiplexing and stochastic computing
  Dual modular redundancy (DMR) and triple modular redundant (TMR)
  Parity bits and Hamming codes

## Slide 3: Faults in Nano-Crossbar Arrays
Ideally
f = A B + C D
Each crosspoint is either closed (diode connected) or open.
What if a crosspoint is closed when it is supposed to be open?
What if a crosspoint is open when it is supposed to be closed?
With a fault
f = A B + B C D
With a fault
f = A + C D
How to tolerate faults?

## Slide 4: Faults in Nano-Crossbar Arrays
Ideally
f = (A B + C D)ꞌ
With a fault
f = 0
How to tolerate faults?
Each crosspoint is either closed (FET or shorted) or open.
What if a crosspoint is closed when it is supposed to be open?

## Slide 5: Faults in Nano-Crossbar Arrays
Each crosspoint is either closed or open depending on the applied literal.
What if a crosspoint is always closed when it is supposed to switch?
What if a crosspoint is always open when it is supposed to switch?
Ideally
f = x1 x2ꞌ x3+ x1 x4ꞌ + x2 x3 x4ꞌ + x2 x4 x5 + x3 x5
0
1
With a fault
f = x1 x2ꞌ x3+ x1 x4ꞌ + x2 x3 x4ꞌ + x2 x4 x5 + x3 x5
With a fault
f = x1 x2ꞌ x3+ x1 x4ꞌ + x2 x3 x4ꞌ + x2 x4 x5 + x3 x5
How to tolerate faults?

## Slide 6: Fault Tolerance Stages
Stages: Fabrication
Stakeholder: Chip Manufacturer
Application Designer
Post-fabrication
In-field/ Service
End User
Mitigation Methods- Adding Redundancy: Error-correcting codes, TMR, NAND demultiplexing
Fabrication, verification and test
Permanent Faults
Permanent+
Transient Faults
Mitigation Methods: Configuring around defects
Mitigation Methods: Self-testing, reconfiguring
Test and verification
Design
Final Product
Nanomaterials: carbon nanotube, nanowires

## Slide 7: Post-fabrication and Defects
Nano-array fabricated with bottom-up methods
In post-fabrication, the ciruit is configured

## Slide 8: Configuration of a circuit
A logic function is implemented with configuration
A full-adder with activating and deactivating the switches
Activated
Deactivated

## Slide 9: Configuration of a circuit
In a defect-free array, straitghtforward process
A B C A B C
A B
B C
A C
A B C
Input Lines
Output Lines
Activated switch
Deactivated switch
O1
O2
O3
O4
O5
O6
O7
I1 I2 I3 I4 I5 I6
F = A B + B C + A C + A B C
(1) Given function
(2) Realized function
F = A B + B C + A C + A B C
Mapping

## Slide 10: Defects
Stuck-at deactivated, switch cannot be activated
Stuck-at activated, switch cannot be deactivated
: Stuck-at deactivated switch
: Stuck-at activated switch
: Configurable switch
: Defective switch

## Slide 11: Mapping with Defects
In a defective array, every mapping is not valid
Activated switch
Deactivated switch
Mapping
A B C A B C
(2) Realized function
A B
A B C
A C
A B C
C
F’ = A B + A B C + A C + A B C + C
Input Lines
Output Lines
O1
O2
O3
O4
O5
O6
O7
I1 I2 I3 I4 I5 I6
(1) Given function
F = A B + B C + A C + A B C
F’
F

## Slide 12: Defect-aware mapping
Mapping is performed with employing defects
B A C A B C
(2) Realized function
A B
B C
A C
A B C
Input Lines
Output Lines
O1
O2
O3
O4
O5
O6
O7
I1 I2 I3 I4 I5 I6
(1) Given function
F = A B + B C + A C + A B C
F = A B + B C + A C + A B C
Activated switch
Deactivated switch
Mapping
A B C A B C
A B
A B C
A C
A B C
C
Previous mapping
F’
F

## Slide 13: Defect-unaware mapping
First, a defect-free sub-array is found
Input Lines
Output Lines
O1
O2
O3
O4
O5
O6
O7
I1 I2 I3 I4 I5 I6 I7
(1) Given function
F = A B + B C + A C + A B C
Defect-free sub-aray
O1
O2
O3
O4
O5
O6
O7
I1 I2 I3 I4 I5 I6 I7
I7 and O5
discarded I7

## Slide 14: Defect-unaware mapping
Second, configuration is starightforward
Input Lines
Output Lines
O1
O2
O3
O4
O5
O6
O7
I1 I2 I3 I4 I5 I6 I7
F = A B + B C + A C + A B C
(1) Given function
Mapping
A B C A B C
A B
B C
A C
A B C
(2) Realized function
F’ = A B + B C + A C + A B C
F’
F

## Slide 15: In-field Transient Faults
Transient faults occur according to a time-domain
They are predicted with probability analysis
Diode and FET Components show different behaviour regarding to the fault type
  Stuck-at OFF: switch is not capable of conducting current, infinite resistance
  Stuck-at ON: switch is constantly conducting current, zero resistance
Diode
Stuck-at OFF only switch
Stuck-at ON entire output line
FET
Stuck-at OFF entire output line
Stuck-at ON only switch

## Slide 16: Diode-based Nanoarray
Stuck-at OFF, no connection between terminals
  Only faulty switch is affected
Stuck-at ON, terminals always connected
  Entire line is affected
: Stuck-at OFF switch
: Stuck-at ON switch
: Functional switch
: Unusable switch
Terminals
Vdd
Gnd

## Slide 17: FET-based Nanoarray
Stuck-at OFF, no connection between terminals
  Entire line is affected
Stuck-at ON, terminals always connected
  Only faulty switch is affected
: Stuck-at OFF switch
: Stuck-at ON switch
: Functional switch
: Unusable switch

## Slide 18: In-field Transient Faults
OFF-to-ON transition fault: The switch is ON when it is supposed to be OFF; x1=0.
ON-to-OFF transition fault: The switch is OFF when it is supposed to be ON; x1=1.
Each switch of the lattice has independent fault rates.

## Slide 19: In-field Transient Faults
Ideally, if x1=0 then all the switches are OFF.
Ideally, if x1=1 then all the switches are ON.
We use redundancy in tolerating faults powered by percolation.

## Slide 20: Percolation Theory
Rich mathematical topic that forms the basis of explanations of physical phenomena such as diffusion and phase changes in materials.
Broadbent & Hammersley (1957).

## Slide 21: Percolation Theory
Sharp non-linearity in global connectivity as a function of random local connectivity.

## Slide 22: Percolation Theory
p2 versus p1 for 1×1, 2×2, 6×6, 24×24, 120×120, and infinite size lattices.
Each square in the lattice is colored black with independent probability p1.
p2 is the probability that a connected path exists between the top and bottom plates.

## Slide 23: Margins
One-margin: Tolerable p1 ranges for which we interpret p2 as logical one.
Zero-margin: Tolerable p1 ranges for which we interpret p2 as logical zero.
Margins correlate with the degree of fault tolerance.

## Slide 24: Implementing Boolean Functions
signals in: xi’s
signals out: connectivity top-to-bottom / left-to-right.

## Slide 25: An Example with 16 Boolean Inputs
A path exists between top and bottom, fL = 1

## Slide 26: Margin Performance with a 2×2 Lattice
fL=x1x3+x2x4 gL =x1x2+x3x4
Different assignments of input variables to the regions of the network affect the margins.

## Slide 27: One-margins (always good)
Fault probabilities exceeding the one-margin would likely cause an (1→0) error.
fL =1
fL =0
ONE-MARGIN

## Slide 28: Good Zero-margins
Fault probabilities exceeding zero-margin would likely cause an (0→1) error.
fL =0
fL =1
ZERO-MARGIN

## Slide 29: Poor Zero-margins
Assignments that evaluate to 0 but have diagonally adjacent assignments of blocks of 1's result in poor zero-margins
fL =0
fL =1
POOR
ZERO-MARGIN

## Slide 30: Lattice Duality
A necessary and sufficient condition for good error margins is that the Boolean functions fL and gL are dual functions.

## Slide 31: Lattice Duality
fL=x1x3+x2x4 gL =x1x2+x3x4
fL ≠ gLD

## Slide 32: Transient Fault Tolerance
Stochastic computing
Randomly shuffled N number of inputs and outputs
Values are calculated as the number of 1 valued input/output lines over N
Parallel operation
Von Neumann’s multiplexing unit, 1956
Values are calculated as the number of 1 valued input/output lines over N
Serial operation

## Slide 33: Multiplexing for Transition Faults
Error probability ϵ : a gate evaluates the incorrect result, the complement of the correct Boolean value, with ϵ.
Calculate z with and without error
ϵ ⟶ ϵ(1-2z)

## Slide 34: Multiplexing for Stuck-at 1 Faults
Calculate z with and without error
ϵ ⟶ ϵ(1-z)
Error/fault probability ϵ : each gate constantly evaluates logic 1 with ϵ.

## Slide 35: Multiplexing for Stuck-at 0 Faults
Calculate z with and without error
ϵ ⟶ ϵ(z)
Error/fault probability ϵ : each gate constantly evaluates logic 0 with ϵ.

## Slide 36: Transient Fault Tolerance
Triple modular redundancy (TMR)
Increase area 2 times plus an XOR gate
For only detection
Dual modular redundancy (DMR)
Increase area 3 times plus XOR gates
For both detection and correction
For only a single output fault
For only a single output fault

## Slide 37: Transient Fault Tolerance
Satisfying Hamming distance
Applicable for large circuits
For only detection
Extra parity bit
For both detection and correction
For only odd number of output faults
Practical for large circuits
For multiple output faults

## Slide 38: Suggested Readings
DeHon, A. (2003). Array-based architecture for FET-based, nanoscale electronics. Nanotechnology, IEEE Transactions on, 2(1), 23-32.
Han, J., & Jonker, P. (2003). A defect and fault-tolerant architecture for nanocomputers. Nanotechnology, 14(2), 224.
Rao, W., Orailoglu, A., & Karri, R. (2007, April). Logic level fault tolerance approaches targeting nanoelectronics plas. In 2007 Design, Automation & Test in Europe Conference & Exhibition (pp. 1-5). IEEE.
Altun, M., & Riedel, M. D. (2011). Robust Computation through Percolation: Synthesizing Logic with Percolation in Nanoscale Lattices. International Journal of Nanotechnology and Molecular Computation (IJNMC), 3(2), 12-30.
Tunali, O., & Altun, M. (2016) Permanent and Transient Fault Tolerance for Reconfigurable Nano-Crossbar Arrays. IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems.