## Slide 1: ELE 523E COMPUTATIONAL NANOELECTRONICS
W3: Reversible Quantum Computing, 3/10/2016
FALL 2016
Mustafa Altun
Electronics & Communication Engineering
Istanbul Technical University
Web: http://www.ecc.itu.edu.tr/

## Slide 2: Outline
Quantum computing
  Gates and circuits
  Algorithms
Reversible circuit design
  Toffoli gate
  Circuit analysis
  Circuit synthesis
  Irreversible to reversible transformation

## Slide 3: Quantum Gates - NOT
Quantum gates are reversible

## Slide 4: Quantum Gates - Hadamard

## Slide 5: Quantum Gates - CNOT
A
B
A′
B′

## Slide 6: Quantum Gates - CNOT
A
B
A′
B′
A | B | A′ | B′
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 0
INPUT | OUPUT
Truth table

## Slide 7: Quantum gates – CCNOT
A
B
C
A′
B′
C′
A | B | C | A′ | B′ | C′
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0

## Slide 8: Quantum gates – CCNOT
A
B
C
A′
B′
C′
Toffoli gate

## Slide 9: Quantum Circuits
There is no way of efficiently preparing the input state.
There is no way of reading out the output precisely.
This is in the nature of measurement in quantum mechanics.
Measurement symbol

## Slide 10: Quantum Circuits
Severe restrictions on measuring and copying signals

## Slide 11: Quantum Circuits
Example:
Find the output quantum states and probabilities.
?
?
How about the truth table?

## Slide 12: Quantum Circuits
Example:
Find the output quantum states and probabilities.
?
?
How about the truth table?

## Slide 13: Factorizing RSA Numbers
RSA numbers are semi-prime numbers. For each RSA number n, there exist prime numbers p and q such that n = p × q.
15 = 3 × 5
77 = 7 × 11
529 = 23 × 23
4633 = 41 × 113
RSA-100 = 15226050279225333605356183781326374297180681
14961380688657908494580122963258952897654000350692006139 =
37975227936943673922808872755445627854565536638199 ×
40094690950920881030683735292761468389214899724061
The prize for RSA-1024 is $100.000.
RSA-2048 takes approximately 10 billion years with the best known algorithm.

## Slide 14: Classical Factorizing
The Classical Algorithm
Arbitrarirly select a number x such that 1<x<n.
Find xi mod n for i = 1,2,3,… until finding the period R.
Calculate greatest common divisor (GCD) of (xR/2 -1, n) and (xR/2 +1, n).
GCDs give the numbers p or q.
Input: A semi-prime number n.
Output: Prime numbers p and q such that n = p × q.
Steps:
What if R is odd?
What if the algorithm results in 1 and n ?

## Slide 15: Classical Factorizing
Example: If n=15 what are p and q?
Arbitrarirly select a number x such that 1<x<n.
  x=7
Find xi mod n for i = 1,2,3,… until finding the period R.
  71 mod 15 = 7
  72 mod 15 = 4
  73 mod 15 = 13
  74 mod 15 = 1
  75 mod 15 = 7
Find GCDs.
  GCD(74/2-1, 15) = 3, GCD(74/2+1, 15) = 5
R = 4

## Slide 16: Classical Factorizing
Example: If n=15 what are p and q?
Arbitrarirly select a number x such that 1<x<n.
  x=9
Find xi mod n for i = 1,2,3,… until finding the period R.
  91 mod 15 = 9
  92 mod 15 = 6
  93 mod 15 = 9
Find GCDs.
  GCD(92/2-1, 15) = 1, GCD(92/2+1, 15) = 5
R = 2

## Slide 17: Classical Factorizing
Example: If n=15 what are p and q?
Arbitrarirly select a number x such that 1<x<n.
  x=14
Find xi mod n for i = 1,2,3,… until finding the period R.
  141 mod 15 = 14
  142 mod 15 = 1
  143 mod 15 = 14
Find GCDs.
  GCD(142/2-1, 15) = 1, GCD(142/2+1, 15) = 15
R = 2

## Slide 18: Classical Factorizing
Example: If n=15 what are p and q?
Arbitrarirly select a number x such that 1<x<n.
  x=10
Find xi mod n for i = 1,2,3,… until finding the period R.
  101 mod 15 = 10
  102 mod 15 = 10
R = 1
Is there a way of properly selecting x ?

## Slide 19: Classical Factorizing
The Classical Algorithm
Arbitrarirly select a number x such that 1<x<n.
Find xi mod n for i = 1,2,3,… until finding the period R.
Calculate greatest common divisor (GCD) of (xR/2 -1, n) and (xR/2 +1, n).
Step-2 is problematic for large numbers.
Shor’s algorithm completes step-2 efficiently.
Step-3 can be done polynomially in time with using Euclidean algorithm.

## Slide 20: Euclidean Algorithm
GCD(7854, 4746) = ?
Euclid, 300 BC
Euclid’s Elements

## Slide 21: Shor’s Algorithm
Time complexity: O((log N)3).
  N is number of digits of the given semi-prime number.
Based on quantum Fourier transform and modular exponentiation.
Success rate is 50%.
Currently no practical and useful implementation.

## Slide 22: Reversible Circuits
Main motivation: energy efficiency.
Energy efficient in error correction and detection.
  Restart or reset a system.
source: http://www.cise.ufl.edu/research/revcomp/

## Slide 23: Reversible Circuits
Toffoli gates with circuit representations
NOT
CNOT
CCNOT
Toffoli
CONTROL
TARGET
1s applied to the control bits makes the target bit negated (flipped)
Work with truth tables and deterministic bits

## Slide 24: Analysis: Circuits to Tables
IN
cba
000
001
010
011
100
101
110
111
OUT
cba
a
b
c
a
b
c
IN
OUT
OUT
cba
100
111
101
110
000
011
010
001

## Slide 25: Analysis: Circuits to Tables
IN
cba
000
001
010
011
100
101
110
111
OUT
cba
a
b
c
a
b
c
IN
OUT
OUT
cba
001
000
011
010
101
111
100
110

## Slide 26: Synthesis: Tables to Circuits
IN
cba
000
001
010
011
100
101
110
111
OUT
cba
001
000
011
010
101
111
100
110
Brute force algorithm
Complexity - how many cases to consider?
(# of gates is upper bounded by 10)

## Slide 27: Synthesis: Tables to Circuits
First Greedy Algorithm:
Step 0.
For the case 000,
If output 000
invert the outputs corresponding to 1 bits with NOT gates.
If output = 000
Do nothing.
Step i.
Using Toffoli gates
-> Shows bits that must be 1 instead of 0
-> Shows bits that must be 0 instead of 1
1- For each , apply Toffoli gates with control lines -> all i=1 at output state target line -> j
2- For each , apply Toffoli gates with control lines -> all i=1 at output state except all «k»’s target line -> k
In
010
110
Out
100
111
Matching input and output rows
Start from the top row and proceed one-by-one to the bottom
Operations on a row should not affect the preceding matched rows

## Slide 28: Synthesis: Tables to Circuits
IN
cba
000
001
010
011
100
101
110
111
OUT
cba
001
000
011
010
101
111
100
110
S1
000
001
010
011
100
110
101
111
S1
000
001
010
011
100
110
101
111
S1
000
001
010
011
100
110
101
111
S2
000
001
010
011
100
111
101
110
S3
000
001
010
011
100
101
111
110
S3
000
001
010
011
100
101
111
110
S4
000
001
010
011
100
101
110
111
a
b
c
a
b
c
IN
OUT
Applying the Algorithm

## Slide 29: Synthesis: Tables to Circuits
Worst Case of the Algorithm

## Slide 30: Synthesis: Tables to Circuits
Second Greedy Algorithm:
Matching input and output rows
Find unmatched rows
Match them arbitrarily using pairwise matchings
Each pairwise matching corresponds to an «essential function»
Essential Functions: Interchange two rows; others are all same
# of essential functions=# of rows choose 2
Bit Size | Functions | 
 | # of Essential Functions | # of Total Functions
2 | 6 | 24
3 | 28 | 40320
4 | 120 | 20922789888000
5 | 469 | 2.613308e + 35
6 | 2016 | 1.268869e + 89

## Slide 31: Synthesis: Tables to Circuits
Input
000
001
010
011
100
101
110
111
0 0 0
0 0 1
0 1 0
1 0 1
1 0 0
0 1 1
1 1 0
1 1 1
1
2
3
4
5
6
7
8
1
2
3
6
5
4
7
8
Input
000
001
010
011
100
101
110
111
1 0 0
0 0 1
0 1 0
0 1 1
0 0 0
1 0 1
1 1 0
1 1 1
1
2
3
4
5
6
7
8
5
2
3
4
1
6
7
8
Input
000
001
010
011
100
101
110
111
1 0 0
0 0 1
0 1 0
1 0 1
0 0 0
0 1 1
1 1 0
1 1 1
1
2
3
4
5
6
7
8
5
2
3
6
1
4
7
8

## Slide 32: Synthesis: Tables to Circuits
# of essential functions = # of unmatched rows -1
Is ordering important? Which essential function to apply?
Top-Down |  |  |  |  |  | Optimum |  |  |  | 
f |  |  |  |  |  | f |  |  |  | 
000 | 0 | 0 | 0 | 0 |  | 000 | 0 | 0 | 0 | 0
111 | 7 | 1 | 1 | 1 |  | 111 | 7 | 3 | 1 | 1
001 | 1 | 7 | 2 | 2 |  | 001 | 1 | 1 | 3 | 2
010 | 2 | 2 | 7 | 3 |  | 010 | 2 | 2 | 2 | 3
100 | 4 | 4 | 4 | 4 |  | 100 | 4 | 4 | 4 | 4
101 | 5 | 5 | 5 | 5 |  | 101 | 5 | 5 | 5 | 5
110 | 6 | 6 | 6 | 6 |  | 110 | 6 | 6 | 6 | 6
011 | 3 | 3 | 3 | 7 |  | 011 | 3 | 7 | 7 | 7
Essential Function | 1-7 | 2-7 | 3-7 |  |  | Essential Function | 7-3 | 1-3 | 2-3 | 
Cost | 4 | 4 | 1 | 9 |  | Cost | 1 | 2 | 2 | 5
 |  |  |  |  |  | Optimum |  |  |  | 
f |  |  |  |  |  | f |  |  |  | 
000 | 0 | 0 | 0 | 0 |  | 000 | 0 | 0 | 0 | 0
111 | 7 | 1 | 1 | 1 |  | 111 | 7 | 3 | 1 | 1
001 | 1 | 7 | 2 | 2 |  | 001 | 1 | 1 | 3 | 2
010 | 2 | 2 | 7 | 3 |  | 010 | 2 | 2 | 2 | 3
100 | 4 | 4 | 4 | 4 |  | 100 | 4 | 4 | 4 | 4
101 | 5 | 5 | 5 | 5 |  | 101 | 5 | 5 | 5 | 5
110 | 6 | 6 | 6 | 6 |  | 110 | 6 | 6 | 6 | 6
011 | 3 | 3 | 3 | 7 |  | 011 | 3 | 7 | 7 | 7
Essential Function | 1-7 | 2-7 | 3-7 |  |  | Essential Function | 7-3 | 1-3 | 2-3 | 
Cost | 4 | 4 | 1 | 9 |  | Cost | 1 | 2 | 2 | 5
(a)
(b)

## Slide 33: Synthesis: Tables to Circuits
Contd.
Is ordering important? Which essential function to apply?
(a)
(b)

## Slide 34: Synthesis: Tables to Circuits
Contd.
Is ordering important? Which essential function to apply?
 | TD | PS | OPT
R.C. | 16.69 | 15.75 | 14.48
Time | 8 | 8 | 377
Complexity |  |  | 
 | TD | PS | OPT
R.C. | 16.69 | 15.75 | 14.48
Time | 8 | 8 | 377
Complexity |  |  | 
Sequence Comparison
TD : Top Down
PS : Pick Smallest
OPT : Optimum
R.C. : Reversible Cost

## Slide 35: Irreversible to Reversible Transformation
Given an irreversible function or truth table:
Having either same or different number of inputs and outputs
Result is a reversible function or truth table:
Might need extra bits (garbage bits)
Larger circuit size
Example: Given a 1-bit full adder, make it reversible.

## Slide 36: Irreversible to Reversible Transformation
Example: Given a 2-to-1 Multiplexer, make it reversible.
What type of functions are more efficient to be transformed?
Don’t care conditions are important and to be reduced.

## Slide 37: Suggested Readings
Nielsen, M. A., & Chuang, I. L. (2010). Quantum computation and quantum information. Cambridge university press.
MIT Technology Review Article, http://www.technologyreview.com/view/422511/the-fantastical-promise-of-reversible-computing/
Maslov, Dmitri, Gerhard W. Dueck, and D. Michael Miller. "Toffoli network synthesis with templates." Computer-Aided Design of Integrated Circuits and Systems, IEEE Transactions on 24.6 (2005): 807-817.
Susam, Omercan, and Mustafa Altun. "Fast Synthesis of Reversible Circuits using a Sorting Algorithm and Optimization" Journal of Multiple-Valued Logic and Soft Computing, accepted for publication, 2016.